## Slide 1
Wafermap Analysis Report
Generated on 2026-02-23 09:06

## Slide 2
Gage R&R Report - Agenda
# | Group | Parameters | Pages | Slides
1 | 📋 Agenda | - | Page 2 | 1
2 | 📖 Calculation Parameters | - | Page 3 | 1
Total: 2 Groups | 0 Parameters | 2 Slides

## Slide 3
Gage R&R - Calculation Parameters
BASIC STATISTICAL VALUES
Mean (Mittelwert):
Average of all measurements across all files and dies.
Mean = Σ(xi) / n
Std Dev (Standardabweichung):
Measure of dispersion around the mean.
σ = √[Σ(xi - Mean)² / n]
Range (Spannweite):
Difference between maximum and minimum.
Range = Max - Min
LSL / USL (Spec Limits):
Statistical limits (k = sigma factor).
LSL = Mean - kσ | USL = Mean + kσ
GAGE R&R COMPONENTS
Repeatability (EV):
Variation within measurements of one file (equipment).
EV = Mean(σ within each file)
Reproducibility (AV):
Variation between files/operators/trials.
AV = σ(file means)
GRR Total:
Combined measurement system variation.
GRR = R̄ / d₂ (Range Method)
ASSESSMENT METRICS
%GRR (Prozent GRR):
GRR as percentage of total variation or tolerance.
%GRR = (GRR / TV) × 100 or (GRR / Tolerance) × 100
ndc (Using Total Variation):
Number of distinct categories the system can distinguish.
ndc = 1.41 × (TV / GRR)
ASSESSMENT CRITERIA (AIAG MSA)
🟢 EXCELLENT: %GRR < 10%
Measurement system is acceptable.
🟡 ACCEPTABLE: 10% ≤ %GRR < 30%
May be acceptable depending on application.
🔴 UNACCEPTABLE: %GRR ≥ 30%
Measurement system must be improved.
ndc ≥ 5: Good measurement system
Can distinguish ≥ 5 distinct categories.
INTERPRETATION
• High Repeatability → Equipment/method problem
• High Reproducibility → Operator/process/time problem
• ndc should be ≥ 5 for a good measurement system
• Values outside LSL/USL indicate outliers